SmartView Versa+ SW Release Notes

Version 2.13

Oct 28, 2009

The latest release of software for the SmartView Versa+ handheld magnifier is version 2.13.  This release corrects some issues related to the unit locking up.

Please visit the Versa support page at:

http://www.humanware.com/versa_support

On the support page you will find links to download the software and documentation including the updated User Guide and these Release Notes.

The update software includes two files contained in a zip file downloaded from the above page.

To update your Versa+

- Unzip the update file on your computer.  There will be two files, one ending in .elf and the other ending in .jpg.

- With a SD card inserted, turn on your Versa+.

- Connect the Versa+ to your computer with the use USB cable.

- Copy the .elf file to the root directory of the SD card.

- Disconnect the Versa+ from the USB cable and computer.

Attention:  During upgrading, ensure that the battery is fully charged or the AC adapter is connected.

- Turn on your Versa+.  While in magnifier mode, press the down arrow button for about 30s until the LED on the front flashes and then release the button.   The message “Firmware is upgrading” will be displayed on the screen.  The Versa+ will turn off automatically.

- Turn on the Versa+ again and go to playback mode.   If there are any saved images either delete them or copy them to your computer before proceeding.

- Press the up arrow for about 30s until the front LED flashes.

- Connect your Versa+ to the computer with the USB cable. You will see a “Resource C” folder appear on your computer.

- Copy the logo.jpg file from the download zip to this folder.

- Disconnect the USB cable.

- Turn on your Versa+.  The software update process is now complete.

# Text boxes

LED

Down Arrow

Up Arrow