Trekker Breeze

GETTING STARTED

HumanWare

1800 Michaud, Drummondville,

Québec, CANADA

J2C 7G7.

Telephone 1-888-723-7273. Fax (819) 471-4828

E-mail: ca.info@humanware.com

Sales: ca.sales@humanware.com

World Wide Web: http://www.humanware.com

Trekker Breeze

Getting Started Instructions

Welcome to the Trekker Breeze, an innovative orientation aid from HumanWare. This Getting Started document will provide a quick overview of the Breeze's features and characteristics. Please consult the User guide for complete instructions.

# Contents of package

Carefully unpack your Trekker Breeze. Save the box and packing materials for future use. Your Trekker Breeze package comprises of the following items:

Trekker Breeze device with 1 Gigabyte SD card installed

Leather case with clip

Shoulder strap

Speaker with clip and cable

Power adapter

USB-PC cable

Lanyard

Getting Started

Companion CD including documentation and software

CD with audio User Guide

- Physical description

# Using Breeze

The Breeze needs to be fully charged before using it the first time.

To charge the Breeze:

1- Connect one end of the supplied Power Adapter to the Breeze's Power connector. The Power connector is located on the bottom right edge of the unit. It is covered by a rubber protective flap.

2- Connect the other end of the Power Adapter to the electrical outlet.

Please allow 5 hours to ensure a full charge.

To get started:

While outside, switch the Power button to On to start Trekker Breeze. After one second, a short beep will be heard, followed 10 seconds later by a system startup message.

A tone will be heard while the system attempts to connect to GPS satellites. When connection is established, the system will announce your current position. Your Trekker Breeze is ready to use. If a connection cannot be established or if it is lost along the way, move to a different location with an unobstructed view of the sky.

To end your Trekker Breeze session, switch the Power button to Off.

Note: You must have an inserted SD card with a map to use Trekker Breeze.

Trekker Breeze uses digital geographical maps to locate your position. These maps are stored on SD cards that you can insert into the Breeze's allotted slot. When powering on the unit, make sure the SD card containing your maps is inserted. The system will activate the first four maps found according to their alphabetical order.

Where am I?

To obtain your current position, press the Where am I button.

What's around

Press and hold the Where am I button to activate the What’s around function. When traveling in streets, points of interest and landmarks found on your current street segment will be announced. Use the left and right arrows to browse the list of landmarks and points of interest.

Select Extended search with the Confirm button to refine your search by selecting a specific category of points of interest to look for. The Breeze will then provide you with a list of up to 50 points of interest found within a range of 5 miles (8 km) that correspond to the selected category. Use the arrows to select the destination of choice, and Confirm to begin turn instructions.

Recording a Route

1. Press and hold the Record button.

2.  Press Confirm to start creating a route. The system will ask you to dictate a route name. After the beep, you will have 4 seconds to describe the route. You may find helpful it to name the route by its origin and destination. For example, Home to pharmacy.

3. When the system has confirmed that you are creating a route, navigate the entire course of the route. Breeze will emit a beep every 60 seconds to indicate the recording of the route. If GPS coverage is lost along the way, a message will inform you and beeping will stop. When GPS coverage is found again, beeping resumes.

4. Note that you can create Landmarks along the way. To do so, press the Record button. After the beep, you will have 4 seconds to provide a vocal description of the landmark. A double beep will indicate the end of the landmark creation, at which point you can continue your route.

5. When you have reached your destination, press and hold the Record button until you hear the beep, to inform the system that the destination has been reached. The beeping stops and a message informs you that Route recording has ended.

Navigate a Recorded Route

You can use Trekker Breeze to guide you along a previously recorded route.

To select a route:

1. Press the Go To button.

2. Use the left and right navigation arrows to browse among available routes.

3. When the route you are looking for is announced, press Confirm. The route is selected and you will be given instructions on the direction to take to begin your route.

## Getting Guidance to an address

To have Breeze guide you to an address:

- Press and hold the Go To button located in the bottom right region of the unit.

- Use the left and right arrows through the list of landmarks and select Enter an address. Press Confirm to select this option.

- The Breeze will ask you to select the state/province in which you will be travelling. Use the Left and Right arrows to make your selection, followed by Confirm.  Note that if a GPS connection is established, the system will automatically suggest the state/province where you are located. Press Confirm to select it.

- You must now enter the name of the city. The previous city name entered will be announced. If you wish to select this city, or if none have been previously entered, you will need to enter the city name or part of it using the Breeze's buttons, then press Confirm. See Entering an address for additional information on how to enter characters. Use arrows to browse the list of names and press Confirm to make your selection

- After entering the city name, you must enter the street name. Proceed using same method as for entering city name.

- Once a street name is entered, you will be asked for a civic number. If you know the exact civic number, again, use the Breeze buttons to enter numbers, followed by Confirm.

If you do not know the exact civic number of your destination, when asked to enter a civic number, simply press Confirm.  At this point, the system will provide a list of address ranges for that given street, followed by a list of intersections where address ranges are not available. Use the Arrows to browse the list, and press Confirm to make your selection.

- At this point, a new landmark will have been created for this address.

- To begin guidance towards this address, when asked, press Confirm again to create a pedestrian route, or press and hold Confirm to begin a Motorized route.

Note: During the character entry process, you can use the Left arrow at any time to delete a character.  If you wish to return to the previous entry level, press Explore. To be reminded of the current level of entry, press Information, and to have your current entry spelled to you, press Repeat.

## Entering an address

When asked to input an address, use the Breeze's buttons to enter the desired information. To do so, press and hold the button that has the letter or number of interest. The letters and numbers will be announced in turn. When the letter/number is announced, simply release the button and proceed with the next character. For example, if you wish to enter the letter K, you would press and hold the Confirm button. At this point, the letter J will be announced, followed by the letter K, at which point you would release the Confirm button.

Each button is assigned letters and numbers as follows:

Information: 1 – '

Where am I?:  A B C 2

Repeat:  D E F 3

Left arrow: G H I 4

Confirm:  J K L 5

Right arrow:  M N O 6

Explore:  P Q R S 7

Record:  T U V 8

Go to:  W X Y Z 9 0 SPACE #

Breeze Button Assignments

While entering an address, the following buttons will perform actions on a single press (press and release).

- Confirm: To make a selection from a list or Confirm after entering a partial name

- Left and Right arrows: Navigation through list, Left to delete previous character.

- Information: Recall current entry field.

- Repeat: Spell current entry field

- Explore: Return to previous level.

# Carrying the Breeze

There are different ways of carrying the Breeze. We recommend you use the shoulder strap to free up your hands when traveling. You can also attach it in front of your hip using the belt clip. However, if you intend on carrying the Breeze in your hand, make sure to adjust the lanyard to your wrist. Also, do not cover the region between the Where am I button and the Confirm button with your hand when holding the Breeze. This could impede signal reception.

Furthermore, you should not use headphones when walking on the street.

In areas with heavy traffic or where the ambient noise makes it difficult to hear the internal speaker, we recommend you wear the external speaker, which can be attached to your shoulder or collar with the clip.

- Key Describer

If you need help remembering what each button does, you can always activate the Key Describer function.

To launch the Key Describer function at any moment, press and hold the Repeat button until you get the message “Key Describer ON”. At this point, you will be able to obtain a general description of each button by simply pressing them.

To exit the Key Describer, press and hold the Repeat button until you get the message "Key Describer OFF".

- Trekker Map Manager

Trekker Map Manager is a PC application that allows you to manage the contents of your storage cards. You can transfer maps, routes and landmarks from the PC to your Breeze storage card. You can also remove Maps from your storage card or create backups of routes and landmarks. You can manage either the landmarks database which contains all the landmarks created by the user or the database containing all P.O.Is from external sources (called External P.O.Is). Please consult the Trekker Map Manage User Guide for additional information.

- Manufacturer Warranty

This device is a high quality product, built and packaged with care. All units and components are guaranteed against any operational defects as follows:

US and Canada: One (1) year

Europe: Two (2) years

Australia and New Zealand: One (1) year

Other countries: One (1) year

Warranty covers all parts (except battery) and labor. If any defect should occur, please contact your local distributor or the manufacturer technical assistance line.

Note: Warranty terms may periodically change, please consult our website for the latest information.

Conditions and Limitations:

No replacement or repair covered by the warranty will be carried out unless the unit is accompanied by a copy of the original bill of purchase. Please retain your original. If the unit has to be returned, please use the original packaging. This warranty applies to all cases where the damage is not a result of improper use, mistreatment, negligence or acts of God.

For customer support, please contact the HumanWare office nearest you or view our Web site at:

http://www.humanware.com/breeze_support

Global: support@humanware.com

North America: 1 (800) 722 3393 or e-mail to us.support@humanware.com

Europe: 01933 415800 or e-mail to eu.support@humanware.com

Australia / Asia: (02) 9686 2600 or e-mail to au.sales@humanware.com

New Zealand: +64 3 384 4555 or e-mail to nz.info@humanware.com