# Victor Reader ClassicX + 3.3

# by HumanWare

Getting Started Session with Victor Reader ClassicX +

Welcome to Victor Reader ClassicX +, your new digital talking book player. The first time you use Victor Reader, you should connect the player to a power outlet.

To connect to a power outlet, plug one end of the provided AC/DC power cord in the power jack. It is located on the back side of the player, slightly to the left of center. Plug the other end of the power cord in an electrical outlet. When first receiving the player or after changing the battery or after an extended storage period, it is best to leave the player plugged into the power outlet overnight to ensure that the battery is fully charged.

Above the Power key is a green LED indicator. The LED indicator will flash when the player is Off and plugged into a power outlet. The flashes indicate that the player is recharging. When it stops flashing, the player is fully charged. When the player is turned On, the LED illuminates continuously, whether it is plugged in or not. Under regular circumstances, the battery takes up to 4 hours to recharge and will provide up to 10 hours playtime for most DAISY books.

Please note that you can use Victor Reader while charging the battery.

The package contains the following items: A Victor Reader ClassicX +, a power cord, a plastic bag with documentation and this CD.  This CD contains a short Getting Started session followed by the User's Guide.

You can pause and resume reading by simply pressing the Play/Stop key, which is located at the bottom center of the player between the Rewind and Fast-Forward keys.

We will now begin the Getting Started session.  Place the player in front of you with the carrying handle on the left.  Above the handle in the top left corner is a built-in speaker.

On the top center of the face are three pairs of up and down keys. From left to right, these are the Tone, Volume and Speed keys.

Beneath the Tone, Volume and Speed keys, you will find a telephone style numeric keypad.  There is a raised dot on the number 5 key. You will use this numeric keypad to move through the structure of a book as well as enter bookmark or page numbers.

To the left of the twelve Numeric keys, about midway down the player, there are two keys. The upper one is the Go To Page key and the lower one is the Bookmark key. The Go To Page key allows you to go directly to a desired page. The Bookmark key inserts bookmarks to save important pages or paragraphs for future reference.

Beneath the twelve Numeric keys you will find, from left to right, the Rewind, Play/Stop and Fast Forward keys.

To the left of the Rewind key and below the Bookmark key, you will find the Sleep key. It is oval shaped and slightly recessed from the surface. It has an amber LED indicator above it.

To the right of the Rewind, Play/Stop and Fast Forward keys and slightly up, you will find two more keys. The upper one, which is slightly recessed, is the Power key and beneath it is the Eject key, used to eject CDs from the drive slot.

On the right side of the player, from back to front, you will find the line out jack (identified with 2 downward tactile marks). It is used to connect the player to a sound system. Next, you will find a remote jack (identified with a single downward tactile mark) to connect to an optional remote switch device for hands-free control of Play/Stop and Rewind functions. Finally near the front is the earphones jack, which can also be used for an external speaker. This jack has an embossed upward tactile mark.

Located at the back of the player, slightly left of center, you will find the power input jack. It is used to connect the player to an electrical outlet.

On the front side of the player you will find the CD-ROM slot drive.

To insert and play a new book

Turn On Victor Reader by pressing and holding the Power key, which is located above the Eject key on the face of the player. You will hear a beep and a Welcome message.

Insert your CD in the slot, which is located on the front side of the player. Gently push the CD forward. The drive mechanism will take over and automatically finish inserting the CD. After a few seconds, Victor Reader will announce the title of the book. To play a book, press the Play/Stop key. If you accidentally insert a CD upside down, it will eject the CD within 15 seconds without damage.

You can adjust the Tone, Volume and Speed by pressing the keys up or down. The Tone, Volume and Speed controls are located on the top center of the face.

To move back or forward at high speed in the book, press and hold the Rewind or Fast-Forward key until you reach the desired spot, then release. The normal playback speed will be resumed.

To pause a reading session

To pause a reading session, simply press the Play/Stop key. To resume reading where you left off, press the Play/Stop key again. Note that if your player is not connected to a power outlet, and if it stays in pause mode for more than 30 minutes, it will shut Off automatically to save the battery.

To end a reading session

To end a reading session, simply turn the player Off by pressing and holding the Power key. Victor Reader will remember where you left off in the book for your next reading session.

To start a new reading session

To start a new reading session in the same book, turn On your Victor Reader by pressing and holding the Power key. After a few seconds, you will hear the title of the book. Press Play to start book.

To eject a CD

To eject a CD, simply press the Eject key. Victor Reader will announce Eject and after a few seconds the motorized mechanism will gently slide the CD out of the drive.

This completes the Getting Started session. The User's Guide will begin playing momentarily.

User’s Guide

About Victor Reader ClassicX +

###### HumanWare is proud to introduce Victor Reader ClassicX +, the powerful digital talking book player.

Victor Reader ClassicX + was designed for leisure reading like best-sellers, novels, magazines, etc. It allows you to easily navigate within the structure and quickly go to desired information.

With its simple to use functions, you can consult the table of contents, go to a section, or return to a bookmark.

We wish you many pleasant hours discovering all the facets of our digital talking book player!

###### Acknowledgement

HumanWare wishes to thank the Canadian National Institute for the Blind (CNIB) Library for recording the Victor Reader ClassicX + Getting Started and User's Guide.

©Copyright 2006. All rights reserved, HumanWare Canada.

This manual is protected by copyright belonging to HumanWare, with all rights reserved. According to copyright law, the manual may not be copied in whole or in part, without written consent from HumanWare.

Table of Contents

1.	Overview of Victor Reader ClassicX +	7

1.1	Unpacking the Player	7

1.2	Physical Description of Victor Reader ClassicX +	8

1.2.1	The Face of the Player	8

1.2.2	The Left Side of the Player	8

1.2.3	The Right Side of the Player	8

1.2.4	The Front Side of the Player	8

1.2.5	The Back Side of the Player	8

1.3	Powering On/Off Victor Reader	8

1.4	Battery	8

1.5	Inserting or ejecting a CD	9

2.	Basic Functions	10

2.1	Control Functions	10

2.2	Play/Stop	10

2.3	Rewind and Fast Forward	10

2.4	Key Describer Mode	10

3.	Numeric Key Functions	11

3.1	Description of Keys	11

3.2	Navigation Keys	12

3.3	Time Jump Navigation Mode	12

3.4	Ten page Jump	12

3.5	Skippable elements	13

3.5.1	Recall skippable elements	13

3.6	Bookshelf — Key 1	13

3.7	History — Key 3	13

3.8	Where am I ? — Key 5	13

3.9	Sleep Mode — Sleep key	13

3.10	Confirm and Cancel — Pound (#) and Star (*) keys	14

3.11	Info — Key 0	14

3.11.1	Available Information Items	14

4.	Advanced Functions	15

4.1	Go to Page	15

4.2	Go to Heading	15

4.3	Bookmarks	15

4.3.1	Going to a Bookmark	15

4.3.2	Inserting a Bookmark	15

4.3.3	Highlight Bookmark	15

4.3.4	Bookmark List	16

4.3.5	Remove Bookmark	17

5.	Configuration Menu – Key 7	18

5.1	Menus and Menu Items List	18

5.1.1	Playback	18

5.1.2	Skip	18

6.	Listening to a Music or MP3 CD	19

6.1	User Interface	19

6.2	Functions	19

7.	Battery Replacement Procedure	20

7.1	Removing battery	20

7.2	Inserting new battery	20

8.	Troubleshooting	21

8.1	Book Navigation	21

8.2	Battery and Charging	21

8.3	CDs	22

8.4	General	23

9.	Technical Specifications	25

# Overview of Victor Reader ClassicX +

## Unpacking the Player

The package contains the following items: A Victor Reader ClassicX +, a power cord, a plastic bag with documentation and this CD.  This CD contains a short Getting Started session followed by the User's Guide. You can print the User’s Guide & Getting Started session if required.

Please ensure that you have received all the items and that none have been damaged in shipping.

Please note that before using Victor Reader for the first time, you need to connect the player to a power outlet. Please note that you can use your Victor Reader while charging the battery.

If any of the above items are missing in the package please contact HumanWare:

Toll Free: 1 888 723-7273 (Canada & U.S.A.)

# Telephone: 1 (819) 471-4818

Fax: 1 (819) 471-4828

# E-mail: ca.support@humanware.com

Website: www.humanware.ca

In some countries the package may also contain a card to fill out if you wish to purchase an optional extension to your basic warranty.  If you find this card and are interested in the extended warranty please note that the card must be returned within 30 days.  If you have difficulty filling out the card or wish more information please contact HumanWare:

Toll Free: 1 888 723-7273 (Canada & U.S.A.)

# Telephone: 1 (819) 471-4818

E-mail: ca.sales@humanware.com

## Physical Description of Victor Reader ClassicX +

### The Face of the Player

On the upper left corner of the player is located the built-in speaker.

On the top center, there are three pairs of up and down keys. From left to right, these are the Tone, Volume and Speed keys.

Beneath the Tone, Volume and Speed controls, you will find the twelve Numeric keys that will allow you to easily move through the structure of a book.

To the left of the twelve Numeric keys, midway down the player, there are two keys. The upper one is the Go To Page key that allows you to go directly to a desired page, the second key is the Bookmark key used to insert a bookmark.

Beneath the twelve Numeric keys you will find the: Rewind, Play/Stop and Fast-Forward keys.

To the left of the Rewind key and below the Bookmark key, you will find the Sleep key. It is oval shaped and slightly recessed from the surface. It has an amber LED indicator above it.

To the right of the Fast-Forward key and slightly up, you will find two more keys. The upper one, which is slightly recessed, is the Power key. Above it you will find a green LED indicator. Beneath the Power key is the Eject key, used to eject CDs from the drive slot.

### The Left Side of the Player

On the left side of the player you will find the built-in handle and speaker.

### The Right Side of the Player

On the right side of the player, from back to front, you will find the line out jack (identified with 2 downward tactile marks). It is used to connect the player to a sound system. Next, you will find a remote jack (identified with a single downward tactile mark) to connect to an optional remote switch device for hands-free control of Play/Stop and Rewind functions. Finally near the front is the earphones jack, which can also be used for an external speaker. This jack has an embossed upward tactile mark.

### The Front Side of the Player

On the front side of the player you will find the CD-ROM drive slot.

### The Back Side of the Player

Located at the back of the player, slightly left of center, you will find the power input jack. It is used to connect the player to an electrical outlet.

## Powering On/Off Victor Reader

To turn the player On, press and hold the Power key, which is the slightly recessed key to the right of the twelve Numeric keys. You will hear a beep and a welcome message.

To turn the player Off, press and hold the Power key again. You will hear two beeps indicating the player is powering Off.

## Battery

The battery is rated for approximately 500 recharge cycles. Under normal conditions the fully charged battery can last up to 10 hours for continuous play of DAISY books, however the battery playtime may be reduced in the following cases :

If the battery is charged for less than 4 hours.

Extensive use of book navigation commands.

Non DAISY CDs take more power and play for about 3 hours on battery power.

High volume level or High Speed playback.

The battery will automatically recharge whenever the player is plugged to AC power. The player can be used while recharging. If the player is powered Off, the power LED indicator will blink if the battery is recharging. A full recharge takes up to 4 hours.

NOTE: When the player is not connected to a power outlet, and staying in pause mode for more than 30 minutes, it will shut Off automatically to save the battery.

## Inserting or ejecting a CD

Insert and gently push the CD forward in the slot located on the front side of the player. A motorized mechanism will slide the CD in the drive. After a few seconds, Victor Reader will announce the title of the book. If you accidentally insert a CD upside down, it will be ejected automatically within 15 seconds without damage.

To eject a CD, simply press the Eject key, located to the right and slightly up from, the Fast Forward key. A motorized mechanism will gently eject the CD from the drive.

NOTE: The Eject key can only work when the Victor Reader is powered On.

# Basic Functions

## Control Functions

Each of the Tone, Volume, and Speed controls has an Up and Down key.  There is a beep to mark the upper and lower range of each control.  If the book is not playing Victor Reader will announce the setting position. For tone and speed there is also a beep to mark the normal or 0 position.  This indicates either a flat tone setting or normal speed setting.

## Play/Stop

To start playing a book, press the Play/Stop key.

To stop playing a book, press the Play/Stop key again.

NOTE: Pressing the Play/Stop key will confirm the current operation (same as pressing the Pound (#) key) and playback will start at the same time.

## Rewind and Fast Forward

These keys allow you to go backward or forward quickly. You will hear the recording at a faster speed.

Press and hold the Rewind or Fast Forward key until you reach the desired spot, the movement of the Rewind or Fast Forward keys will accelerate the longer you hold the key down. For each few seconds you hold the keys you will move forward or backward 1 minute, 2 minutes, 5 minutes, 10 minutes, 15 minutes and so on. The largest jump is 5 minutes. Victor Reader will announce the time jumps and play a normal speed clip between each time jump.

## Key Describer Mode

With the key Describer feature, the user can hear the function associated with each of Victor Reader's keys.  This is especially helpful when learning how to use the player.

If a CD is loaded : Press and hold the Info (0) key to access the Key Describer Mode. The user must press and hold the Info key again to exit the Key Describer Mode.

If no CD is in the drive, The  Key Describer mode will be activated automatically.

While in Key Describer mode you may press any key to hear its function.

# Numeric Key Functions

## Description of Keys

Row one :	1: Bookshelf		2: Navigation Element		3: History

Row two :	4: Back			5: Where am I?			6: Forward

Row three :	7: Menu		8: Navigation Element		9: Not assigned

Row four :	*: Cancel		0: Info				#: Confirm

## Navigation Keys

The 2, 4, 6 and 8 keys are embossed with Up, Left, Right and Down arrows respectively. These keys are navigation keys that allow you to easily go from one structural element (also called navigation level) to another to quickly find desired information.

Victor Reader allows you to navigate by chapter, section, page, time jump, paragraph, or any other existing indexed element defined by the producer of the book.

Use the 2 and 8 keys to choose a navigation level.  These differ from book to book but typically level 1 means chapter, level 2 means section, and level 3 means sub-section and so on. The page element may not be present on all books.  The phrase level is usually the smallest navigation element but this is defined by the book producer.  First, choose a navigation element (chapter, page, etc.), using the 2 and 8 keys.  Then use the 4 and 6 keys to move from the selected element to the previous or next element of the same type.  The 2 and 8 keys will announce only the levels available for the book.  The phrase is always provided but its extent depends on the book producer.

## Time Jump Navigation Mode

Time Jump navigation is available for Daisy books, when enabled, it can be activated using the 2 and 8 keys.

Press the key 2 or key 8 to select the Navigation level, until Victor Reader announces “Time jump” followed by the Jump Delay. Press the key 4 to move Backward or the key 6 to move Forward by the jump interval.

Time Jump delay can be set at 1, 5, 10 minutes. See the Section Configuration Menu for details.

## Ten page Jump

The Ten page Jump feature allows you to move in 10-page jumps to quickly reach a specific page using the Left and Right keys.

Select Page Navigation element by pressing the Up (2) or Down (8) key until you hear “Page”. Then, press and hold the Back (4) or Forward (6) keys. You will hear Victor Reader skip backward or forward in 10-page jumps.

Release the key when you are close to the desired page, then move a page at a time by pressing the Back (4) or Forward (6) keys successively until you reach the desired page.

## Skippable elements

Victor Reader supports the following skippable elements: Footnote, Page number, Production note and Sidebar.

Skippable element can be set as Play, Skip or On Demand, see the Configuration Menu for details. When a skippable element is encountered during playback, Victor Reader behaves as follows:

Play : The element is always played.

Skip : The element is never played.

On Demand : The element is not played but added to the recall list and the element’s name is announced. Note that On Demand option is not available for page and line number elements.

### Recall skippable elements

On Demand skippable elements can be recalled with the Pound key.

Victor reader remembers up to 5 skipped On Demand elements. The last added element will be the first to be recalled. Pressing the Pound key multiple times will recall the prior element in the list. When an element is recalled, the name of the element is played and playback starts at the beginning of the element. When the end of the element is reached, the message “Return to text” is played and the book position will return to where it was when the Pound key was pressed.

During the playback of a recalled element, the user may press Cancel (Star key) to quit playing the recalled element and return to the main text of the book.

## Bookshelf — Key 1

Press the Bookshelf (1) key to access the bookshelf, Victor Reader announces the number of books on the CD and title of the current book.  The keys 4 and 6 allow you to move from title to title to choose the book you want.  Confirm the choice with the Pound (#). You may also confirm selection by pressing the Play key; Victor Reader will start to play from where you left off in the selected book.

## History — Key 3

Pressing key 3 allows you to quickly return to places you have recently been. Victor Reader memorizes up to a maximum of the last 5 places.  Regardless of the element involved (navigation to a page, bookmark), Victor Reader will record and list the movements upon demand.  The history will be erased when changing the book.

Press the History (3) key. Press key 4 or key 6 to move from one element to the next. Each time you press the key, you will hear the history level, and playback will begin. When you reach the desired element, press the Pound (#) key to confirm your choice, and exit the History Menu.

To cancel the operation in progress, press the Star (*) key. Victor Reader will return to the previous operation.

## Where am I ? — Key 5

The Where am I ? key, key 5, has a tactile dot to help locate it. Once pressed, the Where am I? key will let you know where you are at any time without interrupting the reading process. Victor Reader will announce the page, the heading and the title of the current section.

## Sleep Mode — Sleep key

The Sleep Mode key lets you program a delay period, after which the player will shut down automatically.

Press the Sleep Mode key to program a shutdown delay of 15 minutes. Each additional “Sleep Mode” keystroke will add 15 minutes delay, up to a maximum of 60 minutes. The next key press will disable the Sleep Mode and the cycle starts over. A constant amber LED will illuminate above the Sleep Mode key when it is activated. When the sleep cycle reaches its last minute, the LED will start to blink until the player shuts down.

NOTE: Pressing the Sleep key when it has already been activated will tell you the time remaining in Sleep mode. If pressed again, Sleep mode will jump to the next 15 minute increment.

## Confirm and Cancel — Pound (#) and Star (*) keys

The Pound (#) key allows you to confirm an operation.

The Star (*) key allows you to cancel an operation.

## Info — Key 0

The Info (0) key gives direct access to various information.  There are two ways to access the desired information.

Press the Info (0) key. Victor Reader will list all the available items sequentially.

or

Press the Info (0) key. Press key 4 or key 6 to move from one item to another.

To cancel the Info messages, press the Star (*) key.

NOTE: You can also press and hold the Info key to activate Key Describer Mode, see Section 2.4 for details.

### Available Information Items

Book title

Number of pages and total time

Playtime elapsed and playtime remaining

Number of Bookmarks set in the book

Total Headings in the book

Number of books on the current CD ROM

Whether the player is operating on battery or AC power, if on AC power, whether the battery is charging or not charging

Current Battery Level: High, Medium,  Low and Very Low

Victor Reader model number, software program version number, user key(s) (if any), and serial number.

# Advanced Functions

## Go to Page

# The Go to Page function allows you to go directly to a desired page.

Press the Go to Page key, the upper one in the left column. Enter a page number. Press the Pound (#) key to go to the selected Page, Victor Reader will confirm the entered Page number. Or press the Play/Stop key to have Victor Reader start playback from the chosen page.

To cancel, press the Star (*) key.

## Go to Heading

Go to Heading function allows you to go directly to a desired heading. This is useful for books that do not have page markers. For example, you could jump directly to a chapter by going to its heading number rather than advancing chapter by chapter.

Press Go to Page  key twice, (this key is used to toggle between Go to Page and Go to Heading functions). Enter a Heading number. Press the Pound (#) key to go to the selected Heading, a voice message will confirm the Heading number. Or to start reading from the chosen Heading, Press the Play/Stop  key.

To cancel press the Star (*) key.

## Bookmarks

Bookmarks allow you to return to a place quickly and easily.  You can place a virtually unlimited number of bookmarks in the same book. The Bookmark key lets you insert and return to bookmarks, hear them listed or remove them.

### Going to a Bookmark

Press the Bookmark key, once or until you hear ‘go to bookmark’. Enter the number of the bookmark you wish to go to. Press the Pound (#) key. Victor Reader will go to the bookmark and  announce its number. Or, press the Play/Stop key. Victor Reader will go to the requested bookmark and begin playback.

To cancel, press the Star (*) key.

### Inserting a Bookmark

Press the Bookmark key, twice or until you hear ‘insert bookmark’. You can also access this function by holding the Bookmark key down instead of pressing it twice. Enter the number from 1 to 99998 that you wish to assign to the Bookmark. Press the Pound (#) key to confirm or the Play/Stop key to confirm and start playback.  The bookmark will be stored in memory.

To cancel, press the Star (*) key.

NOTE: If you confirm without entering a number, Victor Reader will assign the first available bookmark number.

NOTE: If you enter 99999 as the bookmark number, an invalid entry message will be announced and the action will be cancelled, since this number is reserved to remove all bookmarks. See Remove Bookmark.

### Highlight Bookmark

Highlight Bookmarks are used to define the Start and the End positions of a desired text block to be read subsequently.

#### Start Highlight Bookmark

Press the Bookmark key, 3 times or until you hear “Start highlight bookmark”.

Enter a bookmark number. Press the Pound (#) key to confirm.  If the Play/Stop key was used to confirm, playback will be started.

To cancel, press the Star (*) key.

NOTE: If no number was entered, Victor Reader will assign the first available bookmark number.

#### End Highlight Bookmark

After setting the starting position, navigate to the point where you wish to mark the end of the highlight.

Press the Bookmark key, 3 times or until you hear “End highlight bookmark”. The current position is set as the ending position. If the end position is placed before the start position, they will be switched. The message "Highlight bookmark X inserted" is then played. The user can also cancel the highlight bookmark by pressing the Cancel key. The message "Cancelled" is then played. In both cases, the state reverts to Start. Press the Pound (#) key or Play/Stop key to confirm.  If the Play/Stop key was used to confirm, playback will be started.

To cancel, press the Star (*) key.

NOTE: When a highlight bookmark starting position is set but not the ending position, its highlight bookmark number becomes unavailable. Victor Reader will announce “Bookmark X already exists”  if the user enters a regular bookmark with this number.

NOTE: If ejecting the CD or powering Off the Victor player before closing the highlight, highlight will be cancelled.

#### Go to Highlight Bookmark

When going to a highlight bookmark, If the bookmark exists, the current position is set to the highlight bookmark starting position. If using Play/Stop key, playback will start from this current position and stop at the highlight bookmark ending position. If the Confirm key was used, only the voice message “Highlight Bookmark X” will be played.

#### Highlight Bookmark List

When a highlight bookmark is reached with the bookmark list, playback will stop at the highlight bookmark ending position. A highlight that was started but hasn’t been closed yet will not be listed.

#### Remove Highlight Bookmark

When deleting a highlight bookmark, the "Highlight bookmark X removed" message will be announced. It is possible to delete a highlight bookmark that was started but not closed. This action reverts the highlight bookmark state to Start.

### Bookmark List

Press the Bookmark key, four times or until you hear ‘bookmark list’.

Press the key 4 or key 6 to go from one bookmark to the next. Each time you press the key, you will hear the number of the next bookmark and playback will begin. Press the Pound (#) key to confirm the current position and continue play.

Press the Star (*) key to quit the Bookmark list.

NOTE: The bookmark list always contains one bookmark for the beginning and end of book.  Bookmarks are sorted by their position in the book not by the bookmark number.

### Remove Bookmark

Press the Bookmark key, five times or until you hear ‘remove bookmark’. Enter the number of the Bookmark you wish to remove. Press the Pound (#) key to confirm.

To cancel, press the Star (*) key.

To remove all the Bookmarks in a book, first press the Bookmark key five times or until you hear ‘remove bookmark’, then press the key 9 five times (enter number 99999). Then press the Pound (#) key to confirm.

# Configuration Menu – Key 7

The Victor Reader can be customized using the Configuration menu.

To open the Menu, press the Menu (7) key. Pressing the Menu key again will switch to the next Menu. Browse Menu Items with the Up/Down (2, 8) keys, use the Left/Right (4, 6) keys to select an Item’s value and press Pound key to confirm. Press Cancel (*) or any other key to exit the Menu.

## Menus and Menu Items List

The list of available menus in their respective order is shown below. Note that the first listed values in the list are the factory default settings.

| Menu | Menu Item | Values |
| --- | --- | --- |
| Playback & Navigation | Playback | Normal, Loop, Random |
|  | Time Jump | 1 minute, 5 minutes, 10 minutes |
| Skip | All | Play, Skip, On Demand, Custom |
|  | Footnote | Play, Skip, On Demand |
|  | Page number | Play, Skip |
|  | Production note | Play, Skip, On Demand |
|  | Sidebar | Play, Skip, On Demand |

### Playback

There are three Playback modes Normal, Loop and Random.

#### Normal

Normal is the default, normal unaltered Playback mode. Note that, the Normal Playback mode will be set by default when changing to a new book.

#### Loop

When selecting the Loop mode, Playback will play repeatedly, it will automatically restart again at the beginning when reaching the end of a book or a CD.

#### Random

When selecting the Random mode, Playback will play randomly all the elements in the list. Once the whole list has been played, Playback will start again at the beginning of the list. Note that the Random playback mode is available only for the MP3 CD and Audio CD books.

### Skip

The Skip Menu contains the configuration options for the skippable elements. Play is the default value.

| Menu Item | Values |
| --- | --- |
| All | Play, Skip, On Demand, Custom |
| Footnote | Play, Skip, On Demand |
| Page number | Play, Skip |
| Production note | Play, Skip, On Demand |
| Sidebar | Play, Skip, On Demand |

Selecting the Custom value allows you to set different options for each of the Skip elements. Otherwise; the option you select applies to all elements.

# Listening to a Music or MP3 CD

Victor Reader is not only a talking book player.  You can also play standard audio CDs and MP3 CDs, allowing you to listen to your favorite music or commercial MP3 books.

NOTE: Folders and Files are used for MP3 CDs only, when playing a Music CDDA only track to track navigation is possible.

## User Interface

When inserting an MP3 CD, Victor Reader will issue the message "Folder X, File Y".

On the Bookshelf list, music or MP3 CDs are announced as “Other Audio“.

## Functions

Navigation: The Left (4) and Right (6) arrows are used to switch to the previous or the next file in the same folder. If current file is the first or the last file of a folder, the Left/Right arrows will switch to the last or the first file of the previous or the next folder respectively.

If the Randomize Playback is set, pressing the Left/Right arrow will switch to the previous/next file in the randomized order.

Only the "File" level is available when the Randomize Playback is enabled.

Where am I?: Pressing the Where am I? key will report the current folder, file number and current file’s playtime elapsed.

Play: Playback is continuous, at the end of the current file Victor Reader will switch to the next file and will stop at the end of the last file in the file list.

Go to file: Press the Go to Page key once Victor Reader will go to a specified file (or track) within the current folder. When pressing the Go to Page key, Victor Reader says “Go to file” for MP3 CDs and “Go to track” for CDDA music CDs.

Enter the file/track number, If no number is entered, default will be the current file/track. Press Confirm to move to the chosen file/track. Or, press Play/Stop to move to the chosen file/track and start playing.

Press Cancel key to cancel the request.

Go to folder: Press the Go to Page key twice Victor Reader will go to a specified folder. When pressing the Go to Page key twice, Victor Reader says “Go to folder”. Enter the folder number. If no number is entered, default will be the current folder. Press the Confirm key to move to the first file of the chosen folder and Victor Reader prompts "Go to file".

The user will then enter the desired file number. If no number is entered, 1 is assumed. Press the Confirm key to move to the chosen file and the message "File X" is announced. Or, press the Play/Stop key to move to the chosen file and start playing.

Press Cancel to cancel the request.

Pressing the Info (0) key will announce the following information :

Number of files and folders

Total play time

Time elapsed

Playing Time remaining

Number of Bookmarks

Battery or Power Cord

Victor Reader model number, software program version number, user key(s) (if any), and serial number.

# Battery Replacement Procedure

Contact HumanWare or your authorized distributor to obtain replacement batteries.

## Removing battery

Place the Victor Reader in front of you.

Flip the Victor Reader upside-down so as to have the back of the device facing you. The player’s handle should be on your left.

Locate the battery compartment cover. Three horizontal tactile ridges indicate the center of the cover. On the left side of the cover is a locking screw.

Use a standard screwdriver to remove the screw from the cover. Hold the device firmly with one hand. With the other, press the three horizontal tactile ridges and pull the cover towards you. Flip the cover and hold it in place. Inside the compartment, locate the battery ribbon. Gently tug at the ribbon to dislodge the battery from the compartment. Remove the battery.

## Inserting new battery

Victor Reader batteries are designed to be mistake-proof, meaning that they can only be inserted one way.

To properly insert it into the compartment, first place the battery flat in front of you.

Make sure that the ribbon is pointing towards you. There is a bump on the right side of the battery to prevent inserting it backwards. Underneath, you will find the battery’s three exposed terminals. Two are located on the left of the ribbon, while the third is on the right.

To insert into the compartment, tilt the back of the battery downwards and push forward and down. The battery will lock into place. When in place, the ribbon should be pointing up to facilitate eventual battery removal.

Shut the battery compartment cover and push forward to close. Fasten the screw to secure the battery cover in place.

Note that the new battery will require about three complete charge/discharge cycles to reach optimal charge capacity.

# Troubleshooting

## Book Navigation

- Why does Victor Reader not always announce the same DAISY levels when I press the Up and Down keys?

The Up and Down keys cycle through the DAISY navigation levels provided by the producer of the book.  Not all DAISY books have the same navigation levels.  For example, your book’s producer may have only inserted level 1 (often used for chapters) marks into the book.  In this case, the Up and Down keys will announce only “level 1” and “phrase”.  A phrase level is always included.  Victor Reader can only navigate at the levels provided by the book producer.  Often, the GOTO PAGE function will not work because many books are produced without DAISY page marks.  Also, the phrase jump is not the same for each book.  Some producers may include a phrase mark for a single sentence while others may markup phrase as an arbitrary time jump.  Still others have converted older cassette books and inserted a phrase as an entire side of one cassette.  For books with little or no DAISY navigation marks, you will need to navigate with the fast forward and rewind keys.  The Rewind key is to the left of the Play/Stop key and the Fast Forward key is to the right of the Play/Stop Key.

- How do I know what DAISY navigation levels are available in my book?

The Victor Reader Up and Down keys will cycle through the levels of navigation available in the book.  Many book producers include a section at the beginning of the book that describes what the DAISY levels correspond to in that book.  Check with your book producer if you are unsure of the book’s navigation features.

- How do I quickly jump to the start or end of a book?

Victor Reader has automatic bookmarks for the beginning or end of the book.  Press the Bookmark key until you hear Victor Reader announce, “Bookmark List”.  Then press the left arrow key until you hear, “beginning of book”.  The beginning of book is always to the left of the first user bookmark.  Similarly, to reach the end of the book press the right arrow in the bookmark list until you hear “end of book”.  The end of book is always to the right of the last user bookmark.  If you have not set any bookmarks then you need only press the left arrow key once in the bookmark list to reach the beginning of the book or press the right arrow once to reach the end.

## Battery and Charging

- How long does it take to charge the Victor Reader battery and how long is the playtime?

It takes up to 4 hours to fully charge the player. Playback time on a full charge is approximately 10 hours.  This is based on continuous play of DAISY books. The expected playtime of 10 hours may be reduced by any of the following:

If the player is charged for less than 4 hours.

Extensive DAISY navigation is done as this causes more frequent use of the CD drive and thus consumes more power.

Playing standard (type CD-DA) music or book CDs.

Playing non DAISY MP3 music or book CDs.

Higher volume consumes more power.

Higher playback speed consumes more power

Ambient temperature may affect battery life

- Can I charge the battery while playing a book?

Yes.  If you plug the Victor Reader into AC power it will always recharge the battery even if you are listening to a book. Note that when the player is powered off and connected to AC power the LED power indicator will blink until the battery is fully charged.

- How can I confirm that I have connected the AC/DC adapter correctly?

To locate the power jack, place the player in front of you, with the handle on the left. The Power jack is situated on the back side, slightly to the left of center. When you connect the AC/DC adapter plug while Victor Reader is On you will hear a short chime.  This confirms you are connected and the battery is charging.  You may also confirm that the power supply is properly connected by pressing the INFO key on the ClassicX or the 0 key on the ClassicX + and listening for the message, “power cord operated”.  When not connected to the AC power these info keys will report that Victor Reader is battery operated.  If you unplug the AC/DC adapter while Victor Reader is powered On you will again hear a short chime confirming power has been disconnected.

- Can I reduce the effectiveness of my battery by under-charging or over-charging?

No.  Victor Reader uses high quality NiMH (Nickel Metal Hydride) rechargeable batteries that do not have a chemical memory like Nickel Cadmium batteries.  The NiMH batteries do not require a specific charging cycle and will not be made less effective by under charging or over charging.

- Can I damage my battery if I leave the power cord connected for a long time?

No.  However, if you are not going to use your Victor Reader for a long time such as being away on vacation it is best to disconnect it from the power mains to avoid potential damage from power surges.

- Can I replace my battery?

Yes. Replacement batteries can be obtained from HumanWare or authorized dealers.

- How many times can I recharge my battery before it requires replacement?

The battery is rated for 500 charge/discharge cycles.  After that it will still recharge but its capacity to retain a charge will decrease.  When the battery no longer maintains a charge it should be replaced.

- What precautions should be taken if I am not planning to use the player for an extensive period of time?

The battery should always be fully charged before storing the player. For a period of time exceeding 3 months, it is best to fully charge the battery and remove it from the player. The player should be kept within a temperature of -20 to 35 Celsius and humidity levels between 5 and 90% without condensation.

## CDs

- What should I do if my CD is stuck and will not eject?

First, try turning Off your Victor Reader and then turning it back On and then pressing eject.  If the On/Off key appears to be not working (no beep is heard when you press it) then hold the On/Off key down for 10 seconds, then release it.  Then hold down the eject key while you again press the On/Off key.  Continue to hold the eject key until you hear, “Welcome To Victor”. Victor Reader should then eject the CD.

- Can I damage my Victor Reader if I insert the CD upside down?

No.  Victor Reader will simply eject the CD.

- Why does my Victor Reader make whining or chirpy sounds every couple of minutes?

This is the normal sound of the CDROM drive while the player is reading information from the CD.  For DAISY CD books, after the CD is read it will spin down to save power and become silent for several minutes until it needs to be read again.  Pressing navigation keys or jumping to a bookmark will also cause the CD to spin-up in order to be repositioned to the new location.

- What should I do if my CD skips or stops playing?

Poor quality CDs or CDs with fingerprints or scratches will often not play properly or not play at all. Eject the CD. Try cleaning it using a soft lint free cloth or CD cleaning cloth, which can be purchased at most stores that sell CDs.  Do not use paper towel or tissues. Clean the surface of the CD from the middle towards the outer edge in straight lines. Do not use a circular motion.  If the CD still does not play, it should be inspected for scratches. Scratched CDs should be returned for replacement.

- Do I need to clean the CD drive or laser reading lens?

No.  The type of drive used in the Victor players does not require cleaning.

- May I attach a Braille or other label to the CD?

No.  The label can adversely affect the balance of the CD as it spins at high speed.  Also, if the label should come loose inside the player it will very likely damage the CD-ROM drive. If you receive a CD with a Braille or other non manufacturer’s label you should remove it.

- Why do I sometimes hear the message, “Please Wait”, when I press a key even though there is a CD loaded?

This may happen if you press keys too soon after inserting the CD or turning On the player.  Victor Reader requires some time to scan the disk and load the DAISY navigation information.  After turning your player On or inserting a CD, you should wait until Victor Reader announces the book title before you press any keys.

- What does the message, “No book on disk” mean?

This is the message Victor Reader issues if it does not recognize the type of CD.  Victor Reader can only play DAISY, MP3, or audio CDs.

- What does the message, “Audio format not supported” mean?

The CD has audio files that Victor Reader recognizes but the files are formatted in a way that is incompatible with the Victor Reader software.  You should notify HumanWare technical support.

- Can I damage my Victor Reader by playing a scratched CD?

No. The CD reading lens does not come in contact with the CD surface so it will not be damaged if the CD is scratched. It will also not be subject to wear from repeated plays as with cassette players.

## General

- What should I do if the On/Off key is not working?

If no beep is heard when you press the On/Off key first ensure the player is plugged into the AC power source.  If the On/Off key is still not working, press and hold it down for 10 seconds.  This will reset the player.  Then press it again and Victor Reader should beep and start normally.

- Can the internal Victor Reader software be updated?

Yes.  When HumanWare upgrades the Victor Reader software, customers are able to install the new software by simply inserting a special upgrade CD into the player, which automatically refreshes its internal software program. The upgrade CD may be obtained from HumanWare customer support, directly downloaded from the HumanWare website, or from some dealers who provide this support.

- Should I delete bookmarks to save memory space?

No. Victor Reader can store over 1500 bookmarks spread over many books. Even if you exceed this large number Victor will replace the bookmarks that were used the least often. So, you only need to delete bookmarks if you do not want them.

- Why does the volume control not work for my headphones?

Be sure your headphones are plugged into the headphone jack and not the line-out jack.  The volume control works only for the headphone jack, which is the jack nearest you on the right side of the player. The line-out jack is for connecting to another device such as a stereo or tape recorder.

- What is the purpose of the Remote jack?

The remote jack is a 2.5mm jack located on the right side of the player. It is located on the right side of the player. It is the second jack from the back and it is marked with a single embossed line. Plugging a push-button (usually a footswitch) into this jack allows the user to control the play/pause and rewind functions remotely. Each time the footswitch is pressed, the play/pause function is toggled. Pressing and holding the Footswitch activates the rewind function.

You may use many types of push-buttons to operate the player’s remote functions. The only requirement is that it needs to be a normally open contact switch. This means that the electrical circuit is closed only when the button is pressed.

# Technical Specifications

- Dimensions:		23.7 X 20.9 X 5.4 cm (9.3 X 8.2 X 2.1 in.)

- Weight:			1.1 kg  (2.42lbs) with battery

- DAISY Formats Supported:	DAISY 2.0 and 2.0.2

DAISY NISO Z39.86 2002

- Battery type:		Rechargeable NiMH battery. 7.2 volts 1800 mAh

- Charging time:		4 hours

- Battery life:			10 hours for continuous play of DAISY MP3 book

- Environmental conditions:	Operating temperature: 10-40 Celsius

Storage temperature: -20-35 Celsius

Humidity (no condensation): 5-90%

- Power Supply:		The supplied power adapter meets power requirements only for

the country in which it was sold.  Check with your dealer for

alternate power adapters used for other countries.

- Coding Algorithms:		PCM, ADPCM, MPEG, MP3, OGG (Ogg Vorbis)

- Power jack			2.5 mm (interior)/ 5.5 mm (exterior)

- Line out, earphone jacks	3.5 mm

- Remote jack		2.5 mm

Note that the Remote jack is intended for the use of any push-button device where the electric circuit is closed when the button is pressed.

For additional information, please contact HumanWare:

Head Office

445, du Parc Industriel

Longueuil, Québec

Canada J4H 3V7

Service

1030, René-Lévesque Blvd.

Drummondville, Québec

Canada J2C 5W4

Telephone: 1 (819) 471-4818

Toll-free (Canada & USA): 1 (888) 723-7273

Fax: 1 (819) 471-4828

# E-mail: ca.support@humanware.com

Website: www.humanware.ca

# Text boxes

2

Navigation

Element

1

Bookshelf

3

History

6

Forward

4

Back

5

Where am I ?

9

8

Navigation

Element

7

Menu

#

Confirm

0

## Info

*

Cancel

2

Navigation

Element

6

Forward

4

Back

8

Navigation Element